## Slide 1: FTICR-MS Data Analysis Tutorial
Bob Danczak
Pacific Northwest National Laboratory

## Slide 2: Organization of this tutorial
Overview of FTICR-MS as a technique, WHONDRS, and how to access WHONDRS data
  What is an FTICR-MS and what does the data look like?
  How is the data handled before it is uploaded?
  Where can you find FTICR-MS data?
Walkthrough of common data analysis pipelines
  Pre-processing data using the ftmsRanalysis R package
  Generating Van Krevelen plots to compare molecular composition
  Comparing molecular properties across samples
Examining other analytical techniques
  Multivariate analyses (i.e., PCA, NMDS)
  The transformation analysis

## Slide 3: Fourier Transform Ion Cyclotron Resonance Mass Spectrometry can detect carbon compounds
Fourier Transform Ion Cyclotron Resonance Mass Spectrometry (FTICR-MS) can detect many carbon compounds due to ultra-high mass resolution and accuracy
  The MagLab has a great overview of the FTICR-MS
  Using these specific masses, we can assign molecular formulas based upon previously compiled databases
Today we will be focusing on downloading data from existing sources, processing it, and generating figures for interpretation
  Pre-processing FTICR-MS has many considerations that we will not be discussing
21T FTICR-MS at EMSL

## Slide 4: FTICR-MS Data and WHONDRS
WHONDRS (Worldwide Hydrobiogeochemistry Observation Network for Dynamic River Systems) collects samples from hydrologically dynamic rivers throughout the world via distributed sampling
  Many data types, including FTICR-MS, are collected from each sample
  Data is uploaded to ESS-DIVE for public use
  As part of WHONDRS, we pre-process the data so researchers can take the data and answer the questions that interest them
whondrs.pnnl.gov

## Slide 5: Downloading WHONDRS data from ESS-DIVE
All WHONDRS FTICR-MS data will be available DOE’s ESS-Dive data archive (data.ess-dive.lbl.gov/data)

## Slide 6: Downloading WHONDRS data from ESS-DIVE
All WHONDRS FTICR-MS data will be available DOE’s ESS-Dive data archive (data.ess-dive.lbl.gov/data)

## Slide 7: Downloading WHONDRS data from ESS-DIVE
All WHONDRS FTICR-MS data will be available DOE’s ESS-Dive data archive (data.ess-dive.lbl.gov/data)

## Slide 8: Downloading WHONDRS data from ESS-DIVE
All WHONDRS FTICR-MS data will be available DOE’s ESS-Dive data archive (data.ess-dive.lbl.gov/data)
All the FTICR-MS data will be contained within this folder

## Slide 9: How do we process the data obtained from ESS-DIVE
The data contained within WHONDRS data packages undergone some processing but needs additional adjustments to be useful
  For this we use a program called Formularity (Tolic et al., 2017 – Anal. Chem.)
  This program will calibrate peaks, assign molecular formulas, and allow data to be analyzed together
    Important FTICR-MS caveat: this data provides molecular formula, not compounds as no structural information is provided
Formularity will create a ‘report’ which is used for all downstream analyses
  This report includes molecular formulas, samples, etc. and is used in downstream analyses

## Slide 10: Let’s Generate a Formularity Report
Formularity requires Windows, so those running MacOS or Linux can’t participate unfortunately
Drag and Drop
Calibration_List.ref
WHOI Molecular Formula Database
Formularity supports dragging and dropping of necessary files
First, we need to load up the calibration list and molecular formula database
Drag and Drop

## Slide 11: Let’s Generate a Formularity Report
Formularity requires Windows, so those running MacOS or Linux can’t participate unfortunately
Ensure CIA is checked
Under Calibration
  Start tolerance, ppm: 5
  Regression: linear
Under Formula Assignment
  Alignment: Checked
  Alignment tolerance, ppm: 0.5
  Max relationship gaps: 2
Set the User-defined filter:
  O>0 AND (N+S+P)<6 AND S<3 AND P<2

## Slide 12: Let’s Generate a Formularity Report
Formularity requires Windows, so those running MacOS or Linux can’t participate unfortunately
Drag and Drop
Once you drop the .xml files onto the now green “Drop Spectra Files” box, Formularity will begin to get to work
  It may seem like nothing is happening, but in a few minutes you should have two files in the directory containing the .xml files
  Report.csv and a .log file

## Slide 13: The Formularity report contains a lot of information
Mass
Stoichiometry
Composition
Class
Neutral
Mass
Error
Formula
Candidates
Samples

## Slide 14: Organization of this tutorial
Overview of FTICR-MS as a technique, WHONDRS, and how to access WHONDRS data
  How is the data handled before it is uploaded?
  Where can you find FTICR-MS data?
  What does the data look like?
Walkthrough of common data analysis pipelines
  Pre-processing data using the ftmsRanalysis R package
  Generating Van Krevelen plots to compare molecular composition
  Comparing molecular properties across samples
Examining other analytical techniques
  Multivariate analyses (i.e., PCA, NMDS)
  The transformation analysis

## Slide 15: Hands-on Data Analysis Tutorial
Today we walk through data pre-processing and will cover example analytical techniques
  The provided data is from the Columbia River and has already been processed using Formularity
  Today’s focus is on figure generation and data interpretation to help everyone think of ways they could use FTICR-MS data
All scripts and instructional material for this tutorial can be found on GitHub (https://github.com/danczakre/ICRTutorial)
  The necessary files can be found in the “AGU CZO:Watershed Workshop 2019” folder
  You will need both R and RStudio to ensure the smoothest operation, but no coding experience is needed today
    Some coding knowledge will be required if you wish to modify analyses for your data, however
    Please copy/paste the commands in the “install_packages_commands_updated.txt” after installing R/RStudio
  These scripts and this PowerPoint will remain on GitHub after this tutorial concludes

## Slide 16: Data Pre-processing
This is a quick view of the FTMS_Analysis.R which utilizes the ftmsRanalysis package
You should see a pop-up asking you to select the directory containing the Report
This script will generate two files, a Data and Mol file.
Removes peaks with an isotopic signature, and filters based upon a mass range of 200-900 m/z
Pressing the “Source” button will run the entire script

## Slide 17: The ftmsRanalysis package helps generate files which will be used in all downstream analyses
Data
Mol
Two new files should have been generated – take some time to explore them
  The Data file contains the mass-by-site information
  The Mol file contains molecular information for each formula (i.e., stoichiometry, NOSC)
These two files are useful in downstream analsyes
  What types of carbon are present, and do they change through space/time?
  Are the profiles similar or distinct to each other?
We will walk through two specific analyses: generating a Van Krevelen plot and comparing molecular properties
Van Krevelen Plots
Molecular Properties

## Slide 18: Generating van Krevelen plots
Pressing the “Source” button will run the entire script
You should see a pop-up asking you to select the directory containing the Data and Mol files
This script will generate 2 VK plots: one featuring all data and another for the specified sample
This is a quick view of the Generate_VK_Plot.R script

## Slide 19: Van Krevelen plots can reveal broad molecular patterns
Van Krevelen plots are useful in evaluating the overall ‘molecular landscape’ of your samples
  Plots the hydrogen:carbon (H:C) atomic ratio of each compound against the corresponding oxygen:carbon (O:C) atomic ratio
Different boundary sets can reveal molecular formula dynamics
  Combinations of different H:C and O:C values correspond to compound classes
  For example, lignin-like molecular formula seem to constitute a high proportion of the Columbia River
Other boundary sets and coloring schemes can help reveal important patterns in your dataset
All Data

## Slide 20: Generating van Krevelen plots again!
Pressing the “Source” button will run the entire script
You should see a pop-up asking you to select the directory containing the Data and Mol files
This is a quick view of the Generate_VK_Plot.R script
These options will change the output figures – freq_thresh will adjust the minimum frequency for a compound while samp.num will select a specific sample

## Slide 21: Analyzing molecular properties
You should see a pop-up asking you to select the directory containing the Data and Mol files
This is a quick view of the Generate_MolProp_Plot.R script
Pressing the “Source” button will run the entire script
This script will generate 2 plots which track molecular properties through time

## Slide 22: Patterns in molecular properties can reveal ecosystem dynamics
The script will generate two plots:
  One plot tracks the distributions of a given property by sample (here, the Mass of detected compounds)
  The other is a bar chart for the average value of multiple derived properties of each sample
While the distribution of masses is plotted in this boxplot plot, we can look at other variables:
  NOSC (Nominal Oxidation State of Carbon) can give insight into potential thermodynamics
  AI (Aromaticity Index) and DBE (Double-Bond Equivalents) can reveal patterns in compound properties
  Elemental ratios (i.e., H:C, O:C, N:C, P:C) can reveal patterns in molecular formula
  All these metrics are derived from the stoichiometry and are dependent upon formula assignment

## Slide 23: Analyzing molecular properties
You should see a pop-up asking you to select the directory containing the Data and Mol files
This is a quick view of the Generate_MolProp_Plot.R script
Pressing the “Source” button will run the entire script
This script will generate 2 plots which track molecular properties through time
This option will change the individually plotted parameter

## Slide 24: Organization of this tutorial
Overview of FTICR-MS as a technique, WHONDRS, and how to access WHONDRS data
  How is the data handled before it is uploaded?
  Where can you find FTICR-MS data?
  What does the data look like?
Walkthrough of common data analysis pipelines
  Pre-processing data using the ftmsRanalysis R package
  Generating Van Krevelen plots to compare molecular composition
  Comparing molecular properties across samples
Examining other analytical techniques
  Multivariate analyses (i.e., PCA, NMDS)
  The transformation analysis
  Lambda Theory

## Slide 25: Multivariate analyses can reveal broad spatiotemporal trends
Multivariate analyses can reveal important patterns across your datasets
  Principal component analyses (PCA), principal coordinate analysis (PCoA), and non-metric multidimensional scaling (NMDS) analyses are all valid approaches
Here we have a Jaccard-based NMDS of the 7 rivers you’ll be working with this afternoon fitted with derived metrics
  Erpe River appears to be related to peak counts while the Columbia River is related by high NOSC
  Note: When comparing many different samples, data must be converted to presence/absence

## Slide 26: The Transformation Analysis
The ultra-high mass resolution and accuracy of FTICR data enables us to perform a transformation analysis
  By calculating the mass difference between peaks, we use a database to identify putative biochemical transformations
These transformations can be used to construct a transformation network
  We will not be covering this in detail, but differences in networks might be indicate differing biochemical capabilities
Compound 1
(541.1563282 m/z)
Compound 2
(385.0552115 m/z)
Difference of ~156.1011167 m/z
~156.1011167 m/z
=
Arginine
Example of a transformation
Transformation Network

## Slide 27: Differences in biochemical transformations can reveal biogeochemical patterns
By comparing the proportion of different transformation types across groups, biogeochemically relevant patterns can be uncovered
  Past and ongoing research has demonstrated that nitrogen-based transformations might be more important in pore water/hyporheic zones than surface water
  This indicates a potential link between nitrogen requirements and biogeochemistry
Extending these analyses to other ecosystems will help reveal generalizable biochemical patterns
HJ Andrews Exp. Forest, Oregon
Columbia River, Washington
Stegen et al., 2018 – Nat. Comm.
Danczak et al., in prep

## Slide 28: Applying FTICR-MS data to biogeochemical modeling
Using calculations from Hyun Seob Sung, we can measure carbon use efficiency based upon molecular formula
  Using , we can derive the “stoichiometric coefficient” or YCs,i – the number of moles of carbon required to generate biomass
  This afternoon you’ll be calculating these metrics using FTICR-MS data collected by WHONDRS
By tracking carbon use efficiency or the thermodynamic coefficient () through space/time, we can begin predicting respiration rates and investigate biogeochemical cycles
 is the number of times the catabolic reaction runs to produce one C-mole of biomass
Song et al., in prep
Thermodynamic representation of energy coupling
GCat
GAn
GDis
Catabolism
Anabolism
Metabolic
reaction
S(Ed, Ea)
P
Cs, Ns
Biom
Dissipation
(constant fraction)

## Slide 29: Concluding Remarks
Analyzing FTICR-MS data presents some unique challenges, but WHONDRS hopes to break down barriers
  We collect and analyze data according to standardized, consistent protocols for maximum comparability
  Data will be uploaded to public databases as quickly as possible to allow others to answer potentially interesting questions
All the scripts used today will continue to be hosted on the provided GitHub page (https://github.com/danczakre/ICRTutorial)
  Given the challenges of FTICR-MS data analysis, we are planning on expanding this page into a more general walkthrough to help explain other analysis pathways
  There are currently some other analyses hosted from a previous workshop
FTICR-MS data is rich and deep – we are only scratching the surface of its potential

## Slide 30: Acknowledgements
Environmental Molecular Sciences Laboratory (EMSL)
  Nikola Tolic
  Rosey Chu
  Jason Toyoda
Everyone who helped develop FREDA and ftmsRanalysis
  Lisa Bramer
  Allison Thompson
Everyone who sent in samples for WHONDRS
The WHONDRS team
  Amy Goldman
  Vanessa Garayburu-Caruso
  Lupita Renteria
  Josh Torgeson
  Jackie Wells (Ore. St.)
  Joseph Morad
  Sawi Kumar
James Stegen
Emily Graham